## Slide 1: IETF Hackathon BGP CT interop experiment#2 JUNOS interop with IOS-XR using SAFI 128
IETF 115
05-06 Nov 2022
London
(participating remote)

## Slide 2: Hackathon Plan
BGP CT interop using SAFI-128
  https://datatracker.ietf.org/doc/html/draft-ietf-idr-bgp-ct-00
  Try interop between Junos and IOS-XR
IOS-XR doesn’t support SAFI-76 yet. But because SAFI-76 is a SAFI-128 clone, use that to talk to Cisco. And see if intent-based forwarding works end to end.

## Slide 3: What got done
It worked. :)
  Junos private image (hidden knob ‘use-safi-128’)
  BGP-CT route propagated end-to-end across Cisco node.
  Fwd-Intent got preserved across Cisco node.
  Made a Demo video – embedded in this ppt, next slide.

## Slide 4: https://youtu.be/xCNwCqYVM-Q
Hackathon demo video link

## Slide 5: What we learned
Just shows BGP CT can be implemented in other vendors as-well.
The mechanisms are simple, and backward compatible with existing protocol machinery implemented by other vendors.
Hopefully more vendors support and implement BGP-CT.

## Slide 6: Wrap Up
Team members:
Kaliraj Vairavakkalai.
(kaliraj@juniper.net)
Natrajan Venkatraman.
(natv@juniper.net)
Reshma Das.
(dreshma@juniper.net)
First timers @ IETF/Hackathon:
https://youtu.be/xCNwCqYVM-Q
https://github.com/kalirajv/ietf115-hkthn-bgp-ct-exp2